## Slide 1: 长江汽车电子MES系统方案
群电同津厂
TPMS Architecture Training
2020-11-30

## Slide 2: Topic
IT交接内容 | 测试平台，测试剧本，各server的检查，架构，平台数据关系维运注意事项，平台report开发
Hyper-V 2019 转VMware
TPMS 系统冗余/HA 机制
数据后台修改需求?

## Slide 3: 系统部署配置
硬体
  1.CPU: 5117*2
  2.Memory：128G
  3.Network：万兆网卡*4
  4.Storage：2T 10K SAS*3, 300G SSD*2
软体
  Microsoft Hyper-V Server 2019(Client:Win10 Hyper-V Manager)
  Ubuntu 18.04
  MongoDB4.2.3、Postgres、InfluxDB
  NodeJS 8.9.4/Python2.7.17
  Nginx 1.10.3
  RabbitMQ/MQTT
  Grafana/Telegraf/Kettle
  TPMS
IOT Devices
  2 PLC网关 Per Line
  PLC转换模块
Host-1:
VM1-1: IotServer1
OS: Ubuntu 18.05/Telegraf 1.10.4/Grafana/
Python:2.7.17/NodeJS v8.11.1
TV(AMS Kanban)/
DM(AMS Data Manager)
/DataRecord/TSDBService
VM1-2: DeviceSpare
OS: Ubuntu 18.05/Telegraf 1.10.4
Nginx 1.14.0/NodeJS 8.9.4
GraphicsMagick 1.3.23
TPM Dbus/Device/Spare/Alarm/guard/safe
VM1-4: esb1
OS: Ubuntu 18.05/Telegraf 1.10.4
Hazelcast/
KeepAlived/RabbitMQ
VM1-3: PG
OS: Ubuntu 18.05/Telegraf 1.10.4
MongoDB4.2.6(SECONDARY)
PostgreSQL/Kettle
Host-2:
VM2-1: IotMonitor1
OS: Ubuntu 18.05/Telegraf 1.10.4
Python:2.7.17
Alarm/DeviceStatus/
AppService/
OEE/BusAnnounce/SPC
VM2-2: Mongodb
OS: Ubuntu 18.05/Telegraf 1.10.4
MongoDB4.2.6(PRIMARY)
VM2-4: esb2
OS: Ubuntu 18.05/Telegraf 1.10.4
Hazelcast/
KeepAlived/RabbitMQ
VM2-3: InfluxDB
OS: Ubuntu 18.05/Telegraf 1.10.4
MongoDB4.2.6(SECONDARY Hidden)
InfluxDB

## Slide 4: 软件环境
Machine Name | OA IP | Internal IP | Component | Hardware
IotServer1 | 172.25.57.231 | 10.4.100.231 | TV/DM/DataRecord/TSDBService/Alarm/DeviceStatus/AppService/OEE/BusAnnounce/SPC/Telegraf | cpu:16cores dimm:10G OS HDD:50G ssd
IotMonitor1 | 172.25.57.232 | 10.4.100.232 | Agents | 
DeviceSpare | 172.25.57.233 | 10.4.100.233 | TPM Dbus/Device/Spare/Alarm/guard/safe/Nginx/Telegraf | 
Mongodb | 172.25.57.234 | 10.4.100.234 | MongoDB4.2.6/Telegraf | 
PG | 172.25.57.235 | 10.4.100.235 | MongoDB4.2.6/PostgreSQL/Kettle/Drkon/etcd/Telegraf | 
Influxdb | 172.25.57.236 | 10.4.100.236 | MongoDB4.2.6/InfluxDB/Grafana/Telegraf | 
esb1 | 172.25.57.237 vip:172.25.57.239 | 10.4.100.237 vip:10.4.100.239 | Hazelcast/jre1.8/KeepAlived/RabbitMQ/Telegraf | 
esb2 | 172.25.57.238 vip:172.25.57.239 | 10.4.100.238 vip:10.4.100.239 | Hazelcast/jre1.8/KeepAlived/RabbitMQ/Telegraf | 

## Slide 5: TPM模块图
TPM DB
(MongoDB)
Device Service
Spare Service
Dbus Service
DM Service
Rabbit MQ
AMS DB
(PostgreSQL)
AMS TSDB
(InfluxDB)
Kettle
TPMS Kanban
TV Kanban
IoT Agent
OEE Service
Alarm Service
Data Recorder
TSDB Recorder
Device Status
AMS MemDB
(Hazelcast)
PLC Gateway
工控机Gateway
Guard Service
Safe Service
Telegraf
TPMS Resource Monitor

## Slide 6: 锡炉监控方案(log)
锡炉工控机
RabbitMQ
OEE Service
TV Kanban
TSDB Recorder
Alarm Service
RawData
(InfluxDB)
AMS DB
(PG)
WSM Agent Query (10s)
Device Status
Param Monitor
Event/Data(10s)
Data Recorder
WSM Agent
Log Files
Output Log(30s)
DM
Service

## Slide 7: IOT Deployment in Chicony Product Line
線體 | 站點 | 設備數量 | Switch Port | Mac | IP | 物理接線 | 機台入網狀態 | Log輸出或PLC接入 | TPMS監控
A07 | 插件機 | 1 | 2F7-D006 | B4-96-91-5B-B3-10 | 10.4.92.61 | Done | Done | Log Done | Done
 | 錫爐 | 1 | 2F7-D010 | 04-0E-3C-2B-15-2B | 10.4.92.62 | Done | Done | Log Done | Done
 | 前移載 | 1 | 2F7-D062 |  | PLC网关 LAN1:10.4.92.63 2F7-D062 LAN2:192.168.3.232 | Done | Done | PLC Done | Done
 | AOI | 1 | 2F7-D061 | 00-19-0F-43-4B-49 | 10.4.92.64 | Done | Done | Log Done | Done
 | ICT | 2 | 2F7-D062 |  | PLC网关 LAN1:10.4.92.63 2F7-D062 LAN2:192.168.3.232 | Done | Done | PLC Done | Done
 | ACT | 2 | 2F7-D062 |  | PLC网关 LAN1:10.4.92.63 2F7-D062 LAN2:192.168.3.232 | Done | Done | PLC Done | Done
 | 後移載 | 1 | 2F7-D062 |  | PLC网关 LAN1:10.4.92.63 2F7-D062 LAN2:192.168.3.232 | Done | Done | PLC Done | 監控程式OK。待停線廠商更新PLC程式
 | 組裝 | 16 | 2F7-D023 | C4-00-AD-5A-4E-24 | 10.4.92.65 | Done | Done | Log Done | Done
 | 超音波 | 1 | 2F7-D063 | 00-E2-69-2B-EC-93 | 10.4.92.66 | Done | Done | Log Done | Done
 | BurnIn | 4 | 2F7-D066 |  | PLC网关10.4.92.67 LAN1:10.4.92.67 2F7-D068 LAN2:192.168.3.233 2F7-D067 | Done | Done | PLC Done | Done
 | PD測試 | 1 | 2F7-D067 |  | PLC网关10.4.92.67 LAN1:10.4.92.67 2F7-D068 LAN2:192.168.3.233 2F7-D067 | Done | Done | PLC Done | Done
 | Mapping | 1 | 2F7-D069 |  | PLC网关10.4.92.67 LAN1:10.4.92.67 2F7-D068 LAN2:192.168.3.233 2F7-D067 | Done | Done | PLC Done | 監控程式OK。待停線廠商更新PLC程式

## Slide 8: IOT Deployment in Chicony Product Line
線體 | 站點 | 設備數量 | Switch Port | Mac | IP | 物理接線 | 機台入網狀態 | Log輸出或PLC接入 | TPMS監控
A01 | 錫爐 |  | 2F1-D010 | 00-E0-4C-68-9D-9B | 10.4.92.1 | Done | Done | Log Done | Done
 | 前移載 | 1 | 2F1-D063 |  | PLC网关 LAN1:10.4.92.2 2F1-D063 LAN2: 192.168.3.230 | Done | Done | PLC Done | 監控程式OK。待停線廠商更新PLC程式
 | AOI |  | 2F1-D062 | 00-1B-21-C9-8C-20 | 10.4.92.3 | Done | Done | Log Done | 
 | ICT | 2 | 2F1-D063 |  | PLC网关 LAN1:10.4.92.2 2F1-D063 LAN2:192.168.3.230 | Done | Done | PLC Done | 
 | ACT | 2 | 2F1-D063 |  | PLC网关 LAN1:10.4.92.2 2F1-D063 LAN2:192.168.3.230 | Done | Done | PLC Done | 
 | 後移載 | 1 | 2F1-D063 |  | PLC网关 LAN1:10.4.92.2 2F1-D063 LAN2:192.168.3.230 | Done | Done | PLC Done | 
 | 組裝 | 22 | 2F1-D021 | C4-00-AD-44-89-B3 | 10.4.92.4 | Done | Done | Log Done | Done
 | 超音波 | 1 | 2F1-D026 | 00-E2-69-27-4B-F8 | 10.4.92.5 | 已接入RS232轉網絡模塊，可抓取數據；待安裝供電插板 |  |  | 
 | 超音波 | 1 | 2F1-D027 | 00-E2-69-27-5D-35 | 10.4.92.7 | 已接入RS232轉網絡模塊，可抓取數據；待安裝供電插板 |  |  | 
 | 上机站 | 1 | 2F1-D065 |  | PLC网关 LAN1:10.4.92.6 2F1-D066 LAN2:192.168.3.231 2F1-D065 | Done | Done | Log Done | Done
 | BurnIn | 1 | 2F1-D065 |  | PLC网关 LAN1:10.4.92.6 2F1-D066 LAN2:192.168.3.231 2F1-D065 | Done | Done | Log Done | Done
 | PD測試 | 1 | 2F1-D065 |  | PLC网关 LAN1:10.4.92.6 2F1-D066 LAN2:192.168.3.231 2F1-D065 | Done | Done | Log Done | Done

## Slide 9: IOT Deployment in Chicony Product Line
線體 | 站點 | 設備數量 | Switch Port | Mac | IP | 物理接線 | 機台入網狀態 | Log輸出或PLC接入 | TPMS監控
A08 | 錫爐 |  | 2F8-D010 | 04-0E-3C-28-5E-0B | 10.4.92.72 | Done | Done | Log Done | Done
 | 超音波 |  | 2F8-D061 | 00-E2-69-2B-D3-E3 | 10.4.92.76 | Done | Done | 待與設備工程師設定輸出及開啟共享 | 
A09 | 錫爐 |  | 2F9-D010 | 04-0E-3C-2B-15-92 | 10.4.92.82 | Done | Done | Log Done | Done
 | 超音波 |  |  |  |  | 設備老舊，待更換 |  |  | 
A10 | 錫爐 |  | 2F10-D010 | 04-0E-3C-28-5E-61 | 10.4.92.92 | Done | Done | Log Done | Done
 | 超音波 |  | 2F10-D061 | 00-E2-69-2B-EC-AF | 10.4.92.96 | Done | Done | 待與設備工程師設定輸出及開啟共享 | 
A11 | 錫爐 |  | 2F11-D010 | 04-0E-3C-2B-13-D5 | 10.4.92.102 | Done | Done | Log Done | Done
 | 超音波 |  | 2F11-D028 | 00-E2-69-2B-D3-23 | 10.4.92.106 | Done | Done | 待與設備工程師設定輸出及開啟共享 | 
A12 | 錫爐 |  | 2F12-D010 | 04-0E-3C-2B-15-F0 | 10.4.92.112 | Done | Done | Log Done | Done
 | 超音波 |  | 2F12-D028 | 00-E2-69-28-8E-A6 | 10.4.92.116 | Done | Done | 待與設備工程師設定輸出及開啟共享 | 

## Slide 10: IOT Deployment in Chicony Product Line
線體 | 站點 | 設備數量 | Switch Port | Mac | IP | 物理接線 | 機台入網狀態 | Log輸出或PLC接入 | TPMS監控
T01 | 绕线 | 7 |  |  | PLC网关 LAN1:172.25.11.1 LAN2:192.168.100.100 | Done | Done | PLC Done | Done
 | 中转架台 | 1 |  |  |  | Done | Done | PLC Done | Done
 | 激光剥皮 | 2 |  |  |  | Done | Done | PLC Done | Done
 | 锡炉 | 2 |  |  |  | Done | Done | PLC Done | Done
 | 高压机 | 2 |  |  |  | Done | Done | PLC Done | Done
 | 综合测试 | 2 |  |  |  | Done | Done | PLC Done | Done
 | 摆盘机 | 1 |  |  |  | Done | Done | PLC Done | Done
 | 外壳组装 | 2 |  |  | PLC网关 LAN1:172.25.11.2 LAN2:192.168.100.101 | Done | Done | PLC Done | Done
 | 分拣机台 | 2 |  |  |  | Done | Done | PLC Done | Done
 | ATE | 2 |  |  |  | Done | Done | PLC Done | Done
 | 包装 | 1 |  |  |  | Done | Done | PLC Done | Done

## Slide 11: TPMS Portal
Portal Url:
OA: http://172.25.57.231
Internal: http://10.4.100.232

## Slide 12: Hyper-V Server 2019管理
服务端操作 （Hyper-V Server 2019）
  1、服务器开启后，配置计算机名、配置远程管控功能开启、远程桌面开启、ip地址固定
  2、使用powershell命令，开启credssp
    C:\Users\Administrator>powershell
    PS C:\Users\Administrator> Enable-PSRemoting PS C:\Users\Administrator> Enable-WSManCredSSP -role server
  3、关闭防火墙：
  PS C:\Users\Administrator> netsh advfirewall set currentprofile state off
客户端操作 （Win10）
  1、启用Hyper-V管理工具
  2、修改hosts文件：如192.168.100.100 hyper-v-server
  3、客户端工作组不能为“公用”
  Win-设置-网络和Internet-状态-更改连接属性，公用改为“专用”
  4、修改组策略
    gpedit.msc----本地计算机策略----管理工具----系统----凭证分配：允许分配新的凭证用于仅NTLM服务器身份验证
  启用并添加一行值：wsman/HYPER-V-SERVER
  5、powershell执行命令：
  开启winrm：winrm quickconfig
  winrm安全配置：Set-Item WSMan:\localhost\Client\TrustedHosts -Value "HYPER-V-SERVER"
  winrm身份验证配置：Enable-WSManCredSSP -Role client -DelegateComputer "HYPER-V-SERVER"
参考URL
https://blog.csdn.net/weixin_30293135/article/details/101113957
https://blog.csdn.net/pkgfs/article/details/107090378

## Slide 13: TPMS Server Monitor
Telegraf上报资源数据
Grafana Kanban
http://172.25.57.236:3000/d/7asd4fa567sd4/tpms-server-monitor

## Slide 14: Database Management
MongoDB 4.2.6, Robo 3T 1.3.1管控

## Slide 15: Database Management
InfluxDB 1.7.9, InfluxDBStudio-0.1.0管控

## Slide 16: Database Management
Postgres 11.8, PGAdmin4.3管控